## Slide 1: Introduction to Heat Transfer
Finite Difference Methods
Or
Computational Calculus

## Slide 2: The Microwave Oven
Consider the problem of heating your lunch in a microwave oven
  Given a known heating rate, calculate the time and temperature of your lunch
Is this answer helpful? Does it represent the real world? Take a bite – why is the center cold (frozen) and edges burning hot? Treating the problem as uniform temperature does not work. This problem needs the tools of calculus.

## Slide 3: Computational Calculus
Break up space into small pieces (cells or zones)
Solve simple equations on each cell
As the cell size goes to zero, the solution approaches the correct values
We will use the Introduction to Finite Difference Methods for Numerical Fluid Dynamics by Scannapieco and Harlow to see how to write a computational heat transfer code.

## Slide 4: 1D Heat Flow Domain Discretization
We will read through Chapter II, pages 6-17 and construct the numerical model given there
Page 6
  Note breaking up rod into zones or elements. Each zone will be an element in an array that we declare
  Note definition of finite difference
*Discretization is just a fancy way of saying break into small zones (literally make discrete)

## Slide 5: 1D Heat Flow Definitions and Fick’s Law
Page 7
  Definition of flux and conservation
    Flux is the motion of something from one cell to another
    Conservation is keeping the same total amount of things like mass and energy. This keeps simulations from being non-physical.
Page 8
  Note the equation for an individual cell (zone)
  Fick’s Law is what you should see in high school physics and should be intuitive

## Slide 6: 1D Heat Flow Computational Model
Bottom page 8 and top page 9
  The full model is shown with jbar cells
  Temperatures are defined at cell centers (j)
  Fluxes occur at interfaces between cells (j-½,j+½)
  Boundary cells are added at each end for simplicity in implementing boundary conditions (array size will be 0 to j+1
Bottom page 9, top 10
  Note the equations – simple, but lets check them
  These define energy for this problem – we will want to conserve this energy

## Slide 7: 1D Heat Flow Time Discretization
Page 10 – middle top
  In this section, the time domain is broken up into small pieces for the computation. This is similar to what was done with the space dimension and also uses calculus concepts of breaking things into pieces.
  Note the superscript represents time, not a power
  The time step, dt, must be small enough that all of the heat does not flux out of any cell (a little more complicated than this, but it gets the basic concept).

## Slide 8: 1D Heat Flow Equation for a single zone
Bottom page 10 to top page 11
  Refer back to the diagram for a single cell or a single cell and its two neighbors
  We do a “black box” solution where we don’t worry about what is going on inside a cell and just calculate what is crossing the boundaries
  Write the equations for these fluxes and insert into Fick’s law.
  Rearrange so that Tn+1 is on the left (actually dT or the change in temperature for the cell)

## Slide 9: 1D Heat Flow The Calculus
Section C
  We will skip this section and leave it for you to read through. It uses calculus to come up with the same equation
  But we will take a quick look at equations II-18 and II-19 and replace ∂T with Tn+1-Tn, ∂x with dx and ∂t with dt. Move dt over to the right and it becomes the same as II-12. II-19 is Fick’s Law as written in calculus

## Slide 10: 1D Heat Flow Computational Implementation
Declare an array size j+1
Set initial temperature value
Set boundary conditions on ghost zones (0 and j+1)
Compute new temperatures as shown on pg 16. Note use of T and Tnew and discussion.
Loop back up to setting boundary condition and repeat until we reach time of interest
Print out temperature array

## Slide 11: Sample Implementations
Class will write a code in Python or C and see if they can get the results shown on pgs 17-19. Note scales are 0-50 for x axis and 0-400 for y axis.
Advanced
  Data can be imported into Excel or other plotting programs for a better graph
  Real-time visualization routines can be used to view the simulation during the calculation

## Slide 12: C Code
#include <stdio.h>
int main(int argc, char *argv[]){
int j, jbar=50; // Problem settings
double dx=1.0, dt=0.1, sig=1.0, endtime=10.0, time=0.0, TL=400.0, TR=0.0;
double T[jbar+1], Tnew[jbar+1]; // Declare arrays
for (j = 1; j <=jbar; j++){ T[j] = 0.0;} // Initialize to zero temperature
while (time < endtime){ // Loop until time of interest
  T[0] = 2.0*TL – T[1]; T[jbar+1] = 2.0*TR-T[jbar]; // Set boundary conditions
  for (j=1; j<= jbar; j++) {
    Tnew[j] = T[j] + sig*dt*(T[j+1]+T[j-1]-2.0*T[j])/dx/dx; // Fick’s Law
  }
  for (j=1; j<= jbar; j++) { T[j]=Tnew[j]; } // Move data back to original array
  time += dt; // Advance time
}
for (j=1; j<=jbar; j++) {printf(“x %lf T %lf\n”,((double)j+0.5)*dx,T[j]); } // print results
}

## Slide 13: C++ Code (no objects)
#include <iostream>
#include <vector>
using namespace std;
int main(int argc, char *argv[]){
int jbar=50; // Problem settings
double dx=1.0, dt=0.1, sig=1.0, endtime=10.0, time=0.0, TL=400.0, TR=0.0;
vector<double> T[jbar+1], Tnew[jbar+1]; // Declare arrays
for ( int j = 1; j <=jbar; j++){ T[j] = 0.0;} // Initialize to zero temperature
while (time < endtime){ // Loop until time of interest
  T[0] = 2.0*TL – T[1]; T[jbar+1] = 2.0*TR-T[jbar]; // Set boundary conditions
  for (int j=1; j<= jbar; j++) {
    Tnew[j] = T[j] + sig*dt*(T[j+1]+T[j-1]-2.0*T[j])/dx/dx; // Fick’s Law
  }
  for (int j=1; j<= jbar; j++) { T[j]=Tnew[j]; } // Move data back to original array
  time += dt; // Advance time
}
for (j=1; j<=jbar; j++) {cout << "x " << ((double)j+0.5)*dx << " T " << T[j] << "\n"; }
}

## Slide 14: Fortran code
program heat
integer :: j, jbar=50 ! Problem settings
double precision :: dx=1.0, dt=0.1, sig=1.0, endtime=10.0, time=0.0
double precision :: TL = 400.0, TR = 0.0
double precision :: T(0:jbar+1), Tnew(0:jbar+1) ! Declare arrays
T(:) = 0.0 ! Initialize to zero
do
if (time >= endtime) exit
T(0) = 2.0*TL - T(1) ! Boundary conditions
T(jbar+1) = 2.0*TR - T(jbar)
do j=1,jbar
Tnew(j) = T(j) + sig*dt*(T(j+1)+T(j-1)-2.0*T(j))/dx/dx ! Fick’s Law
enddo
T(1:jbar) = Tnew(1:jbar) ! Move data back to original array
time = time+dt ! Advance time
enddo
do j=1,jbar
print *,"x ",(dble(j)+0.5)*dx," T ", T(j) ! Print results
enddo
end program

## Slide 15: Results from 1st case
x 1.500000 T 364.403880
x 2.500000 T 294.969983
x 3.500000 T 230.553041
x 4.500000 T 173.699977
x 5.500000 T 125.958989
x 6.500000 T 87.809097
x 7.500000 T 58.791526
x 8.500000 T 37.777208
x 9.500000 T 23.283011
x 10.500000 T 13.758309
x 11.500000 T 7.792707
x 12.500000 T 4.229989
x 13.500000 T 2.200338
x 14.500000 T 1.096845
x 15.500000 T 0.524013
x 16.500000 T 0.239960
x 17.500000 T 0.105345
x 18.500000 T 0.044346
x 19.500000 T 0.017905
x 20.500000 T 0.006936
x 21.500000 T 0.002578
x 22.500000 T 0.000920
x 23.500000 T 0.000315
x 24.500000 T 0.000104
x 25.500000 T 0.000033
x 26.500000 T 0.000010
x 27.500000 T 0.000003
x 28.500000 T 0.000001
x 29.500000 T 0.000000
x 30.500000 T 0.000000
x 31.500000 T 0.000000
x 32.500000 T 0.000000
x 33.500000 T 0.000000
x 34.500000 T 0.000000
x 35.500000 T 0.000000
x 36.500000 T 0.000000
x 37.500000 T 0.000000
x 38.500000 T 0.000000
x 39.500000 T 0.000000
x 40.500000 T 0.000000
x 41.500000 T 0.000000
x 42.500000 T 0.000000
x 43.500000 T 0.000000
x 44.500000 T 0.000000
x 45.500000 T 0.000000
x 46.500000 T 0.000000
x 47.500000 T 0.000000
x 48.500000 T 0.000000
x 49.500000 T 0.000000
x 50.500000 T 0.000000

## Slide 16: Further Investigations
Time step stability is discussed starting on pg. 20. You can try this with the class model
Fluid dynamic models of various types are discussed in later chapters.
Simple turbulence models are studied.
And now we can study the microwave problem – does it help to put more heat at the surface (Increase TL)? What is the fastest way to heat the food? the most energy efficient? the most even heating?